## Slide 1
FLOWMLLAB • WEEK 2.1
Probabilistic uncertainty
for CFD surrogates
From a loss function to a calibrated predictive distribution
Notes: Communication job: by the end, students should distinguish prediction error from predictive uncertainty and be able to audit a CFD surrogate distribution on untouched physical cases.
[Sources]
- https://github.com/Ehsan-Roohi/FlowMLLab
[/Sources]

## Slide 2
A point estimate cannot express confidence
WEEK 2.1 • 2 / 14
SAME MEAN ERROR, DIFFERENT SCIENTIFIC RISK
ŷ(x)
One best guess
narrow interval (same scale)
wide interval (twice the width)
The mean can be identical while the decision should change.
Notes: Ask students which prediction they would trust near a wall or operating limit. Emphasize that RMSE alone does not communicate the width or calibration of a predictive distribution.
[Sources]
- https://doi.org/10.1198/016214506000001437
[/Sources]

## Slide 3
Week 2.1 extends supervised regression
WEEK 2.1 • 3 / 14
Week 2 already gives us
features and targets
scaling
losses
case-wise splits
This increment adds
1 write an observation model
2 compute posterior prediction
3 score the full distribution
4 calibrate without touching blind cases
No new neural architecture is required.
Notes: This is intentionally Week 2.1: the lesson depends on Week 2 regression and splitting concepts, then prepares students to interpret uncertainty in later surrogate models.
[Sources]
- https://github.com/Ehsan-Roohi/FlowMLLab/blob/main/COURSE_MAP.md
[/Sources]

## Slide 4
Uncertainty has three different causes
WEEK 2.1 • 4 / 14
ALEATORIC
Noise or unresolved variability
More data may not remove it.
EPISTEMIC
Limited knowledge of the map
More informative data can reduce it.
DISCREPANCY
The simulator misses reality
A confident surrogate can still be wrong.
Do not collapse these mechanisms into one unexplained error bar.
Notes: Use measurement noise, sparse Reynolds-number sampling, and CFD model-form error as concrete examples. The distinction determines what a reported interval can legitimately mean.
[Sources]
- https://doi.org/10.1111/1467-9868.00294
- https://gaussianprocess.org/gpml/
[/Sources]

## Slide 5
A likelihood turns loss into a modeling choice
WEEK 2.1 • 5 / 14
y = fθ(x) + ε
ε ~ 𝒩(0, σ²)
GAUSSIAN OBSERVATION MODEL
−log p(y | θ, σ²)
= n log σ + constant + SSE / 2σ²
For known fixed σ, minimizing NLL in θ is equivalent to MSE. If σ is learned, retain n log σ.
Notes: Derive the negative log likelihood up to an additive constant. Ask when constant variance is implausible in a CFD field—for example, near steep gradients or sparse operating regimes.
[Sources]
- https://gaussianprocess.org/gpml/
[/Sources]

## Slide 6
Bayesian linear regression is an exact update
WEEK 2.1 • 6 / 14
PRIOR
Plausible before data
w ~ 𝒩(m₀, S₀)
LIKELIHOOD
Evidence from data
y | w ~ 𝒩(Φw, σ²I)
POSTERIOR
Plausible after data
w | y ~ 𝒩(mₙ, Sₙ)
Posterior precision = prior precision + data precision
Notes: The notebook computes this update for a noisy Poiseuille velocity profile. The analytic solution lets students inspect every assumption before moving to Gaussian processes.
[Sources]
- https://gaussianprocess.org/gpml/
- https://github.com/Ehsan-Roohi/FlowMLLab/blob/main/notebooks/week02_1/Probabilistic_UQ_CFD.ipynb
[/Sources]

## Slide 7
Prediction uncertainty has two terms
WEEK 2.1 • 7 / 14
Var[y* | x*, D]
=
σ²
observation noise
+
φ*ᵀ Sₙ φ*
parameter uncertainty
Report which terms are included. A posterior over weights does not automatically include simulator discrepancy.
Notes: Separate uncertainty in a latent mean from observation noise. Then revisit the taxonomy: neither term here necessarily represents CFD-to-reality discrepancy.
[Sources]
- https://gaussianprocess.org/gpml/
- https://doi.org/10.1111/1467-9868.00294
[/Sources]

## Slide 8
POD compresses field uncertainty
WEEK 2.1 • 8 / 14
1
CFD cases
u(x; Re)
2
POD basis
Φ₁ … Φᵣ
3
Coefficients
a₁(Re)…aᵣ(Re)
4
Gaussian process
p(aⱼ* | Re*)
5
Field distribution
μu(x), σu(x)
Low-rank structure reduces a spatial field to a few probabilistic coefficient functions.
Notes: Explain that FlowMLLab fits independent fixed-kernel Gaussian processes to a rank-4 velocity POD representation. Independence is a simplifying assumption, not a general truth about modal coefficients.
[Sources]
- https://doi.org/10.1146/annurev.fl.25.010193.002543
- https://gaussianprocess.org/gpml/
- https://github.com/Ehsan-Roohi/FlowMLLab/blob/main/results/probabilistic_uq/protocol.json
[/Sources]

## Slide 9
Calibration must stop before the blind gate
WEEK 2.1 • 9 / 14
DEVELOP
Fit POD + GP
Re = 100, 150, 200, 225, 250, 350, 400
CALIBRATE
Scale interval width once
Re = 300
BLIND TEST
Measure without tuning
Re = 175, 275, 375
The split unit is a complete Reynolds-number case—not individual grid nodes.
Notes: Make students identify every decision that must be frozen before opening Re=175, 275, and 375. Pointwise random splits would leak the same physical solution across partitions.
[Sources]
- https://github.com/Ehsan-Roohi/FlowMLLab/blob/main/results/probabilistic_uq/protocol.json
[/Sources]

## Slide 10
Judge accuracy, calibration, and sharpness
WEEK 2.1 • 10 / 14
01
Accuracy
Is the predictive mass near truth?
02
Calibration
Do nominal levels match frequency?
03
Sharpness
Are intervals as narrow as justified?
Optimizing only one can produce a useless distribution.
Notes: A very wide interval can cover everything and still be uninformative. A very sharp interval can look decisive and still be badly miscalibrated.
[Sources]
- https://doi.org/10.1198/016214506000001437
[/Sources]

## Slide 11
Score the distribution, not only its mean
WEEK 2.1 • 11 / 14
GAUSSIAN NEGATIVE LOG LIKELIHOOD
NLL = ½ log(2πσ²) + ½(y−μ)²/σ²
CONTINUOUS RANKED PROBABILITY SCORE
CRPS compares the predictive CDF with the observed step CDF.
Lower is better. Both scores penalize confident errors.
Notes: NLL can be dominated by a few overconfident misses. CRPS has the same units as the target and integrates distribution quality across thresholds. Use both alongside coverage and width.
[Sources]
- https://doi.org/10.1198/016214506000001437
[/Sources]

## Slide 12
Blind evidence beats a polished uncertainty story
WEEK 2.1 • 12 / 14
Notes: Walk from mean error to coverage. The POD–GP mean slightly improves on interpolation, but its uncertainty bands are not calibrated across all blind Reynolds cases.
[Sources]
- https://github.com/Ehsan-Roohi/FlowMLLab/blob/main/results/probabilistic_uq/probabilistic_uq_validation.png
- https://github.com/Ehsan-Roohi/FlowMLLab/blob/main/results/probabilistic_uq/blind_metrics.csv
[/Sources]

## Slide 13
The mean improved; coverage did not
WEEK 2.1 • 13 / 14
Validation-only scaling increased blind 90% coverage, but did not approach the nominal target.
0.333%
Mean POD–GP relative L₂ error
0.414%
Mean interpolation relative L₂ error
65.2%
Calibrated coverage at nominal 90%
Notes: Retain the failure. The calibrated aggregate coverage is 65.2%, up from 61.5%, but far below 90%. Spatial nodes are correlated, so these values are descriptive rather than finite-sample coverage guarantees.
[Sources]
- https://github.com/Ehsan-Roohi/FlowMLLab/blob/main/results/probabilistic_uq/summary.json
- https://github.com/Ehsan-Roohi/FlowMLLab/blob/main/results/probabilistic_uq/calibration.csv
[/Sources]

## Slide 14
WEEK 2.1 • EXIT CHECKLIST
Make the uncertainty claim
as auditable as the mean
□ State what is random
□ Keep physical cases intact
□ Freeze calibration before blind testing
□ Report accuracy, coverage, and width
□ Preserve under-coverage as evidence
Exit prompt
What new data would separate epistemic uncertainty from CFD model discrepancy?
Notes: Close by having students answer the exit prompt before opening Week 4 surrogate models. The notebook is the executable companion to this lecture.
[Sources]
- https://github.com/Ehsan-Roohi/FlowMLLab/blob/main/notebooks/week02_1/Probabilistic_UQ_CFD.ipynb
- https://gaussianprocess.org/gpml/
- https://doi.org/10.1198/016214506000001437
- https://doi.org/10.1111/1467-9868.00294
[/Sources]